Sp3 Status conditions reported to the host		14 June 2005 A.D.

| [0079] driver time out (from PCSC driver) |  |
| --- | --- |
| [007A] user supplied buffer is too small ( from PCSC driver) |  |
| [0080] driver detected error ( from PCSC driver) |  |
| [2A00] latch failed to close | ST_UK |
| [2A01] configuration update failed | ST_UK¦1 |
| [2A02] configuration update failed | ST_UK¦2 |
| [2A03] report problem | ST_UK¦3 |
| [2A04] configuration update failed | ST_UK¦4 |
| [2A05] configuration update failed | ST_UK¦5 |
| [2A06] no icc voltage not defined on connector | ST_UK¦6 |
| [2A07] length != 2 on SAM options setting | ST_UK¦7 |
| [2A08] latch failed to open | ST_UK¦8 |
| [2A09] command aborted by the icc | ST_UK¦9 |
| [2A0A] sleep only supported with card removed | ST_UK¦0xA |
| [2B00] sle4404 invalid address must be even 16 bit boundary | ST_ADD |
| [2C02] no microprocessor icc seated | ST_NCS¦2 |
| [2C03] no memory card seated | ST_NCS¦3 |
| [2C04] no T=1 raw card seated | ST_NCS¦4 |
| [2C05] no card seated to power off | ST_NCS¦5 |
| [2C06] no card seated to request ATR | ST_NCS¦6 |
| [2C07] no card seated to latch | ST_NCS¦7 |
| [2C08] T=1 card unseated | ST_NCS¦8 |
| [2C09] T=0 card unseated | ST_NCS¦9 |
| [2D00] memory card type not supported | ST_MCD |
| [2D01] Card Not Supported | ST_MCD¦1 |
| [2D03] Card Not Supported, wants CRC | ST_MCD¦3 |
| [2F00] fault alarm received--powered card pulled | ST_ALM |
| [6686] 4404, gpm271 or gpm276 no more counter to decrease | ST_NMC |
| [6687] sle4428 or sle4442 report no retries remain | ST_NRT |
| [6688] 4406 or 4428 invalid PSC/secret key presented | ST_PSC |
| [6701] failed to properly reset configuration | ST_DIF¦1 |
| [6704] gpm271 read value different from expected | ST_DIF¦4 |
| [6705] gpm276 byte(s) not successfully erased | ST_DIF¦5 |
| [6706] 4406 invalid length | ST_DIF¦6 |
| [6709] sle4406 value written doesn't match | ST_DIF¦9 |
| [6900] latch function subtype must be 0 or 1 | ST_CMD |
| [6901] no latch hardware configured | ST_CMD¦1 |
| [6902] rdr not configured with a latch | ST_CMD¦2 |
| [6903] reader configured without icc support | ST_CMD¦3 |
| [6904] reader configured without icc support | ST_CMD¦4 |
| [6905] rdr not configured w/ SAM support or SAM conn > 5 | ST_CMD¦5 |
| [6906] reader configured without icc support | ST_CMD¦6 |
| [6907] reader configured without icc support | ST_CMD¦7 |
| [6908] 'R' cmd subtype invalid | ST_CMD¦8 |
| [6909] invalid baud rate value | ST_CMD¦9 |
| [690A] Set C4 cmd legal values only 0-1 | ST_CMD¦0xA |
| [690B] Set C8 cmd legal values only 0-1 | ST_CMD¦0xB |
| [690C] set cmd subtype invalid | ST_CMD¦0xC |
| [690D] cmd not supported on rdr without icc support | ST_CMD¦0xD |
| [690E] invalid cmd response | ST_CMD¦0xE |
| [690F] invalid baud rate value | ST_CMD¦0xF |
| [6910] invalid serial number length | ST_CMD¦0x10 |
| [6911] 'Q' cmd length must be 1 | ST_CMD¦0x11 |
| [6912] 'P' cmd length must be 1 | ST_CMD¦0x12 |
| [6913] 2nd byte of LED cmd must be 30-37 | ST_CMD¦0x13 |
| [6914] invalid value of the memory card type | ST_CMD¦0x14 |
| [6915] invalid value of the memory card type | ST_CMD¦0x15 |
| [6916] 'P' cmd must be 0x30 or 0x32 | ST_CMD¦0x16 |
| [6918] gpm276 cannot erase 0 bytes | ST_CMD¦0x18 |
| [6919] gpm271 count of bytes to erase is zero | ST_CMD¦0x19 |
| [691B] sle4404 cannot erase 0 bytes or odd # of bytes | ST_CMD¦0x1B |
| [691C] sle4404 password must be even # of bytes > 0 | ST_CMD¦0x1C |
| [691D] download code missing or corrupted | ST_CMD¦0x1D |
| [691E] MSR read method must be 1, 2 or 3 | ST_CMD¦0x1E |
| [691F] host LED control not enabled | ST_CMD¦0x1F |
| [6920] reader not configured for buffered mode | ST_CMD¦0x20 |
| [6921] reader not configured for buffered mode | ST_CMD¦0x21 |
| [6922] Reader not configured for magstripe read | ST_CMD¦0x22 |
| [6D01] INS not supported on i2c cards | ST_INS¦1 |
| [6D02] INS not supported on sle4428 cards | ST_INS¦2 |
| [6D03] INS not supported on sle4442 cards | ST_INS¦3 |
| [6D04] INS not supported on gpm271 cards | ST_INS¦4 |
| [6D05] INS not supported on gpm276 cards | ST_INS¦5 |
| [6D06] INS not supported on sle4404 cards | ST_INS¦6 |
| [6D07] INS not supported on sle4406 cards | ST_INS¦7 |
| [6E00] memory card class must be 'DA' | ST_CLA |
| [8001] sle4428 count bytes to verify must be 2 | ST_LEN¦1 |
| [8002] i2c no data or write cnt != byte recvd | ST_LEN¦2 |
| [8003] sle4428 count bytes to read required | ST_LEN¦3 |
| [8004] sle4428 no data or write cnt != bytes recvd | ST_LEN¦4 |
| [8005] i2c count bytes to read required | ST_LEN¦5 |
| [8006] sle4442 count bytes to verify must be 3 | ST_LEN¦6 |
| [8007] sle4428 no data or write cnt != bytes recvd | ST_LEN¦7 |
| [8008] sle4442 count bytes to read required | ST_LEN¦8 |
| [8009] sle4442 count of protection bytes to read must be 4 | ST_LEN¦9 |
| [800A] sle4442 no data or write cnt != byte recvd | ST_LEN¦0xA |
| [800B] sle4442 no data or write cnt != byte recvd | ST_LEN¦0xB |
| [800D] gpm271 count bytes to read required | ST_LEN¦0xD |
| [800E] sle4428 count bytes to read required | ST_LEN¦0xE |
| [800F] gpm276 count bytes to read required | ST_LEN¦0xF |
| [8013] sle4406 count bytes to read required | ST_LEN¦0x13 |
| [8014] sle4404 count bytes to read required | ST_LEN¦0x14 |
| [8015] sle4404 no data or write cnt != byte recvd | ST_LEN¦0x15 |
| [8016] gpm276 no data or write cnt != byte recvd | ST_LEN¦0x16 |
| [8017] gpm271 no data or write cnt != byte recvd | ST_LEN¦0x17 |
| [8018] sle4406 no data or write cnt != byte recvd | ST_LEN¦0x18 |
| [8019] setting mag prefix D2 cmd invalid length | ST_LEN¦0x19 |
| [801A] setting mag postfix D3 cmd invalid length | ST_LEN¦0x1A |
| [801B] setting baud rate invalid length | ST_LEN¦0x1B |
| [8100] icc err time out on power-up req. by Sp2 Driver | ST_TIM |
| [8100] icc error time out on power-up | ST_TIM |
| [8101] icc time out error | ST_TIM¦1 |
| [8200] invalid TS character received | ST_UTS |
| [8300] T=0 parity on header transmission | ST_PET |
| [8301] T=0 parity on transmission | ST_PET¦1 |
| [8400] parity error receiving procedure byte from T=0 card | ST_PER |
| [8500] PPS confirmation error | ST_PPS |
| [8600] Unsupported F, D, or combination of F and D | ST_FD |
| [8700] protocol not supported EMV TD1 out of range | ST_PRT |
| [8800] CPU card power not at proper level | ST_PWR |
| [8801] unable to power memory card | ST_PWR¦1 |
| [8802] T=1 power not at proper level | ST_PWR¦2 |
| [8803] power not at proper level | ST_PWR¦3 |
| [8804] power not at proper level | ST_PWR¦4 |
| [8805] power not at proper level | ST_PWR¦5 |
| [8900] ATR length too long | ST_ATR |
| [8B01] EMV invalid TA1 byte value | ST_TXX¦1 |
| [8B02] if EMV TB1 required | ST_TXX¦2 |
| [8B03] EMV Unsupported TB1 only 00 allowed | ST_TXX¦3 |
| [8B04] EMV Card Error, invalid BWI or CWI | ST_TXX¦4 |
| [8B06] EMV TB2 not allowed in ATR | ST_TXX¦6 |
| [8B07] EMV TC2 out of range | ST_TXX¦7 |
| [8B08] EMV TC2 out of range | ST_TXX¦8 |
| [8B09] per EMV96 TA3 must be > 0xF | ST_TXX¦9 |
| [8B10] icc error on power-up | ST_TXX¦0x10 |
| [8B11] if EMV96 T=1 then TB3 required | ST_TXX¦0x11 |
| [8B12] Card Error, invalid BWI or CWI | ST_TXX¦0x12 |
| [8B13] Card Error, invalid BWI or CWI | ST_TXX¦0x13 |
| [8B17] EMV TC1/TB3 conflict | ST_TXX¦0x17 |
| [8B20] EMV TD2 out of range must be T=1 | ST_TXX¦0x20 |
| [8C00] TCK error | ST_TCK |
| [9000] Success | ST_OK |
| [A000] card is seated | 0xA000 |
| [A301] icc error on power-up current overflow | ST_PCE¦1 |
| [A304] connector has no voltage setting | ST_PCE¦4 |
| [A305] icc error on power-up invalid (sblk(IFSD) xchg | ST_PCE¦5 |
| [A306] icc error on request ATR from CPU icc | ST_PCE¦6 |
| [A307] icc error on power-up at current limit | ST_PCE¦7 |
| [B0xx] card status reporting | 0xB000 ¦ Status |
| [E300] i2c card ack failure | ST_SCE |
| [E301] icc error after session start | ST_SCE¦1 |
| [E302] T=1 icc error (data too long) | ST_SCE¦2 |
| [E303] i2c card ack failure | ST_SCE¦3 |
| [E304] T=1 too many retries to get response | ST_SCE¦4 |
| [E305] 3 byte i2c cmd & MS addr ack failure | ST_SCE¦5 |
| [E306] 3 byte i2c LS addr ack failure | ST_SCE¦6 |
| [E307] 4 byte i2c cmd ack failure | ST_SCE¦7 |
| [E308] 4 byte i2c MS addr ack failure | ST_SCE¦8 |
| [E309] 4 byte i2c LS addr ack failure | ST_SCE¦9 |
| [E30A] i2c failure to reset card | ST_SCE¦0xA |
| [E310] report timeout error | ST_SCE¦0x10 |
| [E401] error sending command to T=0 card | ST_PRB¦1 |
| [E402] error receiving procedure byte from T=0 card | ST_PRB¦2 |
| [E403] T=0 error getting second status byte | ST_PRB¦3 |
| [E404] T=0 inconsistent procedure byte received | ST_PRB¦4 |
| [E405] T=0 error processing block after procedure byte | ST_PRB¦5 |
| [E406] problem receiving proper # bytes from T=0 icc | ST_PRB¦6 |