80068511-001-B

Spectrum III and Secure

Magstripe Only Insert Reader

OPOS User Manual

Revision History

| Revision | Description | Author | Date |
| --- | --- | --- | --- |
| A | Initial Release | Candy H | 11/25/2013 |
| B | Change the software structure | Xinhu Li | 10/12/2015 |

Table of Contents

1.	Description	6

2.	Important Note	6

3.	Target Device	6

4.	Platform	7

5.	Properties, Methods and Events	7

5.1	Properties	7

5.2	Methods	15

5.3	Events	20

6.	Programming Example	22

6.1	Visual C++ 6.0 programming example	22

6.2	Visual Basic 6.0 programming example	24

6.3	Visual Studio 2005 C# programming example	26

7.	Result Code/Error Code List	27

SOFTWARE COPYRIGHT NOTICE

SOFTWARE LICENSE AGREEMENT

("LICENSOR") IS WILLING TO LICENSE THIS SOFTWARE TO YOU ONLY IF YOU ACCEPT ALL OF THE TERMS IN THIS LICENSE AGREEMENT. PLEASE READ THE TERMS CAREFULLY BEFORE YOU AGREE BECAUSE YOU WILL BE BOUND BY THE TERMS OF THIS AGREEMENT. IF YOU DO NOT AGREE TO THESE TERMS, LICENSOR WILL NOT LICENSE THIS SOFTWARE TO YOU.

Ownership of the Software

1.  The Licensor software program ("Software") and any accompanying written materials are owned by Licensor [or its suppliers] and are protected by United States copyright laws, by laws of other nations, and by international treaties.

Grant Of License

2.  Licensor grants to you the right to use the Software in conjunction with an product. You may load one copy into permanent memory of one computer and may use that copy only on that same computer.

Restrictions on Use and Transfer

3.  You may not copy the Software, except that (1) you may make one copy of the Software solely for backup or archival purposes, and (2) you may transfer the Software to a single hard disk provided you keep the original solely for backup or archival purposes. You may not copy the written materials.

4.  You may permanently transfer the Software and any accompanying written materials (including the most recent update and all prior versions) if you retain no copies and the transferee agrees to be bound by the terms of this Agreement. Such a transfer terminates your license. You may not rent or lease the Software or otherwise transfer or assign the right to use the Software, except as stated in this paragraph.

5.  You may not reverse engineer, decompile, or disassemble the Software.

Limited Warranty

6.  If used in conjunction with an LICENSOR product, Licensor warrants that the Software will perform substantially in accordance with the accompanying written materials for a period of 90 days from the date of your receipt of the Software. Any implied warranties on the Software are limited to 90 days. Some states and territories do not allow limitations on duration of an implied warranty, so the above limitation may not apply to you.

7.  LICENSOR DISCLAIMS ALL OTHER WARRANTIES, EITHER EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO IMPLIED WARRANTIES OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE, AND NON-INFRINGEMENT, WITH RESPECT TO THE SOFTWARE AND ANY ACCOMPANYING WRITTEN MATERIALS. This limited warranty gives you specific legal rights. You may have others, which vary from state to state.

8.  LICENSOR'S ENTIRE LIABILITY AND YOUR EXCLUSIVE REMEDY SHALL BE REPLACEMENT OF THE SOFTWARE THAT DOES NOT MEET LICENSOR'S LIMITED WARRANTY. Any replacement Software will be warranted for the remainder of the original warranty period or 30 days, whichever is longer.

9.  This Limited Warranty is void if failure of the Software has resulted from modification, accident, abuse, or misapplication.

10.  IN NO EVENT WILL LICENSOR BE LIABLE TO YOU FOR DAMAGES, INCLUDING ANY LOSS OF PROFITS, LOST SAVINGS, OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES ARISING OUT OF YOUR USE OR INABILITY TO USE THE SOFTWARE. Because some states do not allow the exclusion or limitation of liability for consequential or incidental damages, the above limitation may not apply to you.

11.  This Agreement is governed by the laws of the state of California.

12.  U.S. Government Restricted Rights. The Software and documentation are provided with Restricted Rights. Use, duplication, or disclosure by the Government is subject to restrictions set forth in subparagraph (c)(1) of The Rights in Technical Data and Computer Software clause at DFARS 252.227-7013 or subparagraphs (c)(1)(ii) and (2) of Commercial Computer Software - Restricted Rights at 48 CFR 52.227-19, as applicable.

# Description

The documentation describes the properties, methods, and events of SecureMOIR and Spectrum MOIR. The component includes two parts: a Control Object running on the upper level, which is an ActiveX control, and a Service Control running on the lower level, which is an OLE automation server. The properties, methods, and events are exposed by the Control Object. For example, when the Control Object is imported into your project as an ActiveX control, you will see all the properties, methods, and events.

# Important Note

This document can be applied to RS232, USBCDC, USBHID and USBHID Keyboard interface readers. Besides, PS/2 Keyboard interface is only for MOIR device.

For different interface devices, OPOS driver is the same one. According to different logical name open different interface device.

For the USB HID Keyboard interfaces device, the standard keyboard should not be pressed when swiping cards, otherwise the card data will be wrong , OPOS Driver will display a warning dialog and the data will be discarded .

The “MSR Keyboard Base Driver” doesn’t need to be installed in advance for the USBKB and PS/2 Keyboard interfaces, because the driver is included in the OPOS driver.

The device can’t support hot plug when OPOS driver is in the Open state. If you have already pulled out the device in Open state, close driver and reopen can use again.

The MOIR firmware can’t support JIS cards. If you swipe a JIS card, it will make the device no response. In this case, please restart the device.

Following description is only for 3.08 version.

If can’t open, please change the port for RS232 (default is COM1) and USBCDC (default is COM2) interfaces in the file “cfgcom_Srv.xml” which is in the OPOS driver installation directory(default is C:\Program Files\ID TECH\Secure Mag Only Insert Reader\OPOS Driver Secure Mag Only Insert Reader Series\). At the same time, it can change the OutputDataConversion Mode(default is DEFAULT_MODE) to STANDARD_MODE in the “cfgcom_Srv.xml” file.

- Target Device

TM3 SecureMOIR RS232 Interface

TM3 SecureMOIR USBCDC Interface

TM3 SecureMOIR USBHID Interface: PID is 2510

TM3 SecureMOIR USBKB Interface: PID is 2520

TM3 MOIR RS232 Interface: = TM3 SecureMOIR RS232 Interface(level 1,2)

TM3 MOIR USBCDC Interface: = TM3 SecureMOIR USBCDC Interface(level 1,2)

TM3 MOIR USBHID Interface: PID is 0640

TM3 MOIR USBKB Interface: PID is 0620

MOIR RS232 Interface

MOIR USBCDC Interface

MOIR USBHID Interface: PID is 0640

MOIR USBKB Interface: PID is 0620

MOIR PS/2 Keyboard Interface

# Platform

Microsoft Windows 8 32bit, Windows 7 32bit, Vista 32bit, XP 32bit, 2000, 98
Microsoft Windows 8 64bit, Windows 7 64bit, Vista 64bit
Service Object and Control Object:
Service Object Version: 1.13.200 Dll File Version: 3.2.0.0
Control Object Version:1.13.001

- Properties, Methods and Events

TM3 MOIR and MOIR can’t support encryption and authentication. This section describes methods, properties and events. Please refer to the attachment part.

  - Properties

Please see UPOS Spec if the detailed information is wanted.

NOTE: 	CO --- Control Object

SO --- Service Object

AP or App --- the abbreviation of Application.

Property Group1---Description

| Name | Type | Mutability | Use After | Description | Support? |
| --- | --- | --- | --- | --- | --- |
| DeviceControlDescription | String | read-only | -- | Identify the Control Object and the company that produced it | Yes |
| DeviceControlVersion | int32 | read-only | -- | hold the Control Object version number. | Yes |
| DeviceServiceDescription | String | read-only | open | identify the Service Object supporting the device and the company that produced it | Yes |
| DeviceServiceVersion | int32 | read-only | open | hold the Service Object version number. | Yes |
| PhysicalDeviceDescription | string | read-only | open | identify the device and any pertinent information about it. | Yes |
| PhysicalDeviceName | string | read-only | open | identify the device and any pertinent information about it. | Yes |

Property Group2---Control

| Name | Type | Mutability | Use After | Description | Support? |
| --- | --- | --- | --- | --- | --- |
| Claimed | Boolean | read-only | open | SecureMOIR must be claimed for exclusive use before access its methods and properties, and before any events to be fired. It is initialized to FALSE by the Open method. It is set to TRUE after the method Claim is successfully called. | Yes |
| AutoDisable | Boolean | read-write | open | When TRUE, as soon as an event DataEvent is received, then DeviceEnabled is automatically to FALSE. It is initialized to FALSE by the Open method. | Yes |
| DeviceEnabled | Boolean | read-write | open& claim | When FALSE, SecureMOIR has been disabled and any subsequent input will be discarded (No DataEvent could be received even if the card is swiped). It is initialized to FALSE by the Open method. | Yes |
| FreezeEvents | boolean | read-write | open | When TRUE, events are not required to be delivered and will be held by SO until events are unfrozen. It is initialized to FALSE by the Open method. | Yes |
| DataEventEnabled | boolean | read-write | open | When TRUE, a DataEvent or ErrorEvent will be delivered immediately when had. (Of course , FreezeEvents=FALSE and DeviceEnabled=TRUE is a prerequisit). It is initialized to FALSE by the Open method. | Yes |
| CapPowerReporting | int32 | read-only | open | Identifies the reporting capabilities of the device about Power. It seems that SecureMOIR doesn’t support in the hardware. | No |
| PowerNotify | int32 | read-write | open | Contains the type power notification selection made by the Application. is initialized to OPOS_PN_DISABLED by the Open method. | No |
| PowerState | int32 | read-only | open | Contains the current power condition. It seems that SecureMOIR doesn’t support in the hardware. | No |
| State | int32 | Read-only | -- | Contains the current state of the Control. It can be set to one of the four Values: Closed, Idle, Busy, or Error. | Yes |
| DataCount | int32 | Read-only | open | Holds the number of enqueued DataEvents remained in the queue. | Yes |
| CheckHealthText | string | read-only | open | Holds the results of the most recent call to the CheckHealth method. Before the first CheckHealth method call, its value is uninitialized. | Yes |

Property Group3---Track Control

| Name | Type | Mutability | Use After | Description | Support? |
| --- | --- | --- | --- | --- | --- |
| CapISO | boolean | read-only | open | If TRUE, SecureMOIR supports ISO cards. | Yes |
| CapJISOne | boolean | read-only | open | If TRUE, SecureMOIR supports JIS Type-I cards. JIS-I cards are a superset of ISO cards. Therefore, if CapJISOne is true, it is implied that CapISO is also TRUE. | Yes |
| CapJISTwo | boolean | read-only | open | If TRUE, SecureMOIR supports JIS type-II cards. | Yes |
| CapTransmitSentinels | boolean | read-only | open | If TRUE, SecureMOIR is able to transmit the start and end sentinels. e.g. start sentinel could be ‘%’ or ‘;’, and stop sentinel could be ‘?’. | Yes |
| DecodeData | boolean | read-write | open | If TRUE, each byte of track data properties is mapped from its original encoded bit sequence (as it exists on the magnetic card) to its corresponding decoded ASCII bit sequence. | Yes |
| ParseDecodeData | boolean | read-write | open | When TRUE, the decoded data contained within the Track1Data and Track2Data properties is further separated into fields for access via various other properties. If DecodeData=FALSE, ParseDecodeData must be false. | Yes |
| TransmitSentinels | boolean | read-write | open | If TRUE, the Track1Data, Track2Data, Track3Data, and Track4Data properties contain start and end sentinel values. Otherwise only the track data between these sentinels. | Yes |
| TracksToRead | int32 | read-write | open | Indicate which track data that the App wishes to get following a card sweep. | Yes |
| ErrorReportingType | int32 | Read-write | open | Holds the type of errors to report via ErrorEvents. This property has one of the following values: MSR_ERT_CARD or MSF_ERT_TRACK | Yes |

Property Group4---TrackData

| Name | Type | Mutability | Use After | Description | Support? |
| --- | --- | --- | --- | --- | --- |
| Track1Data | binary | read-only | open | Holds the track 1 data obtained from the most recently swept card. If DecodeData is true, then it has been decoded from the “raw” format. it may also be parsed into other properties when the ParseDecodeData property is set. | Yes |
| Track1DiscretionaryData | binary | read-only | open | Holds the track 1 discretionary data obtained from the most recently swept card. It may be NULL when: 1) The field was not included in the track data obtained, or, 2) The track data format was not supported, 3) ParseDecodeData is false. | Yes |
| Track2Data | binary | read-only | open | Holds the track 2 data obtained from the most recently swept card. If DecodeData is true, then it has been decoded from the “raw” format. it may also be parsed into other properties when the ParseDecodeData property is set. | Yes |
| Track2DiscretionaryData | binary | read-only | open | Holds the track 2 discretionary data obtained from the most recently swept card. It may be NULL when: 1) The field was not included in the track data obtained, or, 2) The track data format was not supported, 3) ParseDecodeData is false. | Yes |
| Track3Data: | binary | read-only | open | Holds the track 3 data obtained from the most recently swept card. | Yes |
| Track4Data | binary | read-only | open | Holds the track 4 data (JIS-II) obtained from the most recently swept card. | No |
| Track1EncryptedData | binary | read-only | Open | Holds the encrypted track 1 data obtained from the most recently swiped card. The start and end sentinel values are contained in it, and appear only after data is decrypted. Encrypted data is always a multiple of 8 bytes (when Encryption Algorithm is 3DES) or 16 bytes (when Encryption Algorithm is AES) in length. And it will be transmitted as a Hex string. Example, 0xAB 0x00 0x09 is converted to "AB0009". | Yes |
| Track1EncryptedDataLength | int32 | read-only | Open | Holds the length of the raw track 1 data before it was encrypted. | Yes |
| Track2EncryptedData | binary | read-only | Open | Holds the encrypted track 2 data obtained from the most recently swiped card. The start and end sentinel values are contained in it, and appear only after data is decrypted. Encrypted data is always a multiple of 8 bytes (when Encryption Algorithm is 3DES) or 16 bytes (when Encryption Algorithm is AES) in length. And it will be transmitted as a Hex string. Example, 0xAB 0x00 0x09 is converted to "AB0009". | Yes |
| Track2EncryptedDataLength | int32 | read-only | Open | Holds the length of the raw track 2 data before it was encrypted. | Yes |
| Track3EncryptedData | binary | read-only | Open | Holds the encrypted track 3 data obtained from the most recently swiped card. The start and end sentinel values are contained in it, and appear only after data is decrypted. Encrypted data is always a multiple of 8 bytes (when Encryption Algorithm is 3DES) or 16 bytes (when Encryption Algorithm is AES) in length. And it will be transmitted as a Hex string. Example, 0xAB 0x00 0x09 is converted to "AB0009". | Yes |
| Track3EncryptedDataLength | int32 | read-only | Open | Holds the length of the raw track 3 data before it was encrypted. | Yes |
| Track4EncryptedData | binary | read-only | Open | Holds the encrypted track 4 data obtained from the most recently swiped card. | No |
| Track4EncryptedDataLength | binary | read-only | Open | Holds the length of the raw track 4 data before it was encrypted. | No |
| AdditionalSecurityInformation | binary | read-only | Open | Holds additional security/encryption information when a DataEvent is delivered. For example “DUKPT sequence number” in it. This data is always 10 bytes in length. And it will be transmitted as a Hex string. Example, 0xAB 0x00 0x09 is converted to "AB0009". | Yes |
| CardAuthenticationData | binary | read-only | Open | Holds card authentication information when a DataEvent is delivered. | No |
| CardAuthenticationDataLength | int32 | read-only | Open | This property will be zero if CapCardAuthentication is an empty string. | No |
| DeviceAuthenticated | boolean | read-only | Open& Claim& Enable | If the device supports authentication the service must keep the value of this property up to date when the device is enabled. MSR_SUE_DEVICE_AUTHENTICATED or MSR_SUE_DEVICE_DEAUTHENTICATED. | Yes |
| CardType | string | read-only | open | Holds the card type identifier for the most recently swiped card. Value is one of them (“BANK”,”AAMVA” and empty). | Yes |
| CardTypeList | string | read-only | open | Holds a comma separated list of string names of card types supported by the Service. Value is BANK and AAMVA. | Yes |
| CardPropertyList | string | read-only | open | Holds a comma separated list of the names of the properties parsed from the most recently swiped card. | Yes |

Property Group5---ParsedData

| Name | Type | Mutability | Use After | Description | Support? |
| --- | --- | --- | --- | --- | --- |
| AccountNumber | string | read-only | Open | Holds the account number obtained from the most recently swept card. it is initialized to NULL if: 1) The field was not included in the track data obtained, or, 2) The track data format was not supported, or, 3) ParseDecodeData is false. | Yes |
| ExpirationData | string | read-only | Open | Holds the expiration date obtained from the most recently swept card. Others are same as AccountNumber. | Yes |
| FirstName | string | read-only | Open | Holds the first name obtained from the most recently swept card. Others are same as AccountNumber. | Yes |
| MiddleInitial | string | read-only | Open | Holds the middle initial obtained from the most recently swept card. Others are same as AccountNumber. | Yes |
| Surname | string | read-only | Open | Holds the surname obtained from the most recently swept card. Others are same as AccountNumber. | Yes |
| Title | string | read-only | Open | Holds the title obtained from the most recently swept card.. Others are same as AccountNumber. | Yes |
| Suffix | string | read-only | Open | Holds the suffix obtained from the most recently swept card.. Others are same as AccountNumber. | Yes |
| ServicCode | string | read-only | Open | Holds the service code obtained from the most recently swept card. Others are same as AccountNumber. | Yes |

Property Group6--- Statistic

| Name | Type | Mutability | Use After | Expected Result | Test Result |
| --- | --- | --- | --- | --- | --- |
| CapStatisticsReporting | boolean | read-write | Open | If true ,the SO can get device information to a XML statistics | No |
| CapUpdateStatistics | Bolean | read-write | Open | If true ,the SO can update the XML statistics | No |

Property Group7---Firmware

| Name | Type | Mutability | Use After | Expected Result | Test Result |
| --- | --- | --- | --- | --- | --- |
| CapCompareFirmwareVersion | boolean | read-write | Open | If true ,the SO can compare the Firmware version | No |
| CapUpdateFirmware | boolean | read-write | Open | If true ,the SO can update the firmware of the device | No |
| CapWritableTracks | Int32 | Read_only | Open | This capability indicates if the SecureMOIR device supports the writing of track data - and which tracks are supported. | No |
| EncodingMaxLength | Int32 | Read_only | Open | The maximum length of data that can be written by the SecureMOIR to the track(s) . | NO |
| TracksToWrite | Int32 | Read-Write | Open | Holds the SecureMOIR track(s) that will be written. | NO |
| CapDataEncryption | Int32 | Read_only | Open | Holds a bitwise indication of the encryption algorithms supported by the device and selectable via the DataEncryptionAlgorithm property. MSR_DE_NONE: Data encryption is not enabled. MSR_DE_3DEA_DUKPT: Triple DES Derived Unique Key Per Transaction. MSR_DE_AES_DUKPT (value:3): Advanced Encryption Standard Derived Unique Key Per Transaction. | Yes |
| DataEncryptionAlgorithm | Int32 | Read-Write | Open& Claim | Holds the encryption algorithm that will be used to encrypt the track data. This property may be set to one of the supported encryption algorithms as defined in the CapDataEncryption property. MSR_DE_NONE: Data encryption is not enabled. | Yes |
| CapTrackDataMasking | boolean | Read_only | Open | This value will be true if the Service is capable of masking track data. | Yes |
| CapCardAuthentication | string | Read_only | Open | Holds the type, if any, of card authentication data that is supported by the device. | NO |
| CapDeviceAuthentication | Int32 | Read_only | Open | Holds the level of device authentication supported by the service. MSR_DA_NOT_SUPPORTED: The service does not support device authentication. MSR_DA_OPTIONAL: The service supports device authentication but does not require it. MSR_DA_REQUIRED:The service requires device authentication. | Yes |
| DeviceAuthenticationProtocol | Int32 | Read_only | Open | Holds the device authentication protocol supported by the device. MSR_AP_NONE:The service does not support device authentication. MSR_AP_CHALLENGERESPONSE:The service supports the challenge response protocol. | Yes |
| WriteCardType | string | Read-Write | Open | Holds the card type to be used the next time the writeTracks method is called. | NO |

## Methods

These function declarations may be different when the Control Object (OPOSMSR.OCX) is imported into your application project. Please see UPOS Spec for more detailed information.

- Open

Syntax 		LONG Open (BSTR DeviceName);

Remarks 	Call to open a device for subsequent I/O.

Device Name:

TM3 SecureMOIR RS232 interface	“IDTECH_SMOIR_RS232”

TM3 SecureMOIR USBCDC interface	“IDTECH_SMOIR_USBCDC”

TM3 SecureMOIR USBHID interface	“IDTECH_SMOIR_USBHID”

TM3 SecureMOIR USBKB interface	“IDTECH_SMOIR_USBKB”

TM3 MOIR RS232 interface	“IDTECH_MOIR_RS232” or “IDTECH_SMOIR_RS232”

TM3 MOIR USBCDC interface	“IDTECH_MOIR_USBCDC” or “IDTECH_SMOIR_USBCDC”

TM3 MOIR USBHID interface	“IDTECH_MOIR_USBHID”

TM3 MOIR USBKB interface	“IDTECH_MOIR_USBKB”

MOIR RS232 interface			“IDTECH_MOIR_RS232”

MOIR USBCDC interface		“IDTECH_MOIR_USBCDC”

MOIR USBHID interface		“IDTECH_MOIR_USBHID”

MOIR USBKB interface			“IDTECH_MOIR_USBKB”

MOIR PS/2 Keyboard interface	“IDTECH_MOIR_PS/2KB”

Support?		Yes

This method finds more parameters in the Windows Register Tables on key or subkeys. Other

parameters are in the XML file “cfgcom_Srv.xml”.

RS232 interface:

Register

[HKEY_LOCAL_MACHINE\SOFTWARE\OLEforRetail\ServiceOPOS\MSR\IDTECH_SMOIR_RS232]

@="IDTechSMOIR.RS232"

XML

<Interface type="SERIAL" port="1" baud="38400" parity="2" datasize="8" datastop="0" OutputDataConversion="DEFAULT_MODE"/>

USBCDC interface:

Register

[HKEY_LOCAL_MACHINE\SOFTWARE\OLEforRetail\ServiceOPOS\MSR\IDTECH_SMOIR_USBCDC]

@="IDTechSMOIR.RS232"

XML

<Interface type="USBCDC" port="2" baud="9600" parity="2" datasize="8" datastop="0" OutputDataConversion=" DEFAULT _MODE"/>

USBHID interface:

Register

[HKEY_LOCAL_MACHINE\SOFTWARE\OLEforRetail\ServiceOPOS\MSR\IDTECH_SMOIR_USBHID]

@="IDTechSMOIR.USBHID"

XML

<Interface type="USBHID" vid="0acd" pid = "2510" OutputDataConversion="DEFAULT_MODE"/>

USBKB interface:

Register

[HKEY_LOCAL_MACHINE\SOFTWARE\OLEforRetail\ServiceOPOS\MSR\IDTECH_SMOIR_USBKB]

@="IDTechSMOIR.USBKB"

XML

<Interface type="USBKB" vid="0acd" pid = "2520" OutputDataConversion=" DEFAULT _MODE"/>

- ClaimDevice 	Added in Release 1.5

Syntax 		LONG ClaimDevice (LONG Timeout);

Remarks 	Call this method to request exclusive access to the device. Many devices require

an application to claim them before they can be used.  Release 1.0 – 1.4 In releases prior to 1.5, this method is named Claim.

Support?		Yes

- CheckHealth

Syntax 		LONG CheckHealth (LONG Level);

Remarks 	Called to test the state of a device.

Support? 	Yes

Description	When select CH_INTERNAL, check the SO response, if not it tells that there is something wrong with the device. CheckHealthText property will be “Internal HCheck: Successful”

When select CH_EXTERNAL, SO will return the firmware version of the SecureMOIR device, if reading the firmware version is successful. CheckHealthText property will be “External HCheck: Successful” + firmware version information. If Not Responding, CheckHealthText property will be “External HCheck: Not Responding ”.

When select CH_INTERACTIVE , SO will display a dialog , which include firmware version and swiping card . And it can display the “Real data ” of the card , include Start Sentinel and End Sentinel. CheckHealthText property will show “External HCheck:: HCheck: Complete” , after close the dialog .

- ClearInput

Syntax 		LONG ClearInput ();

Remarks 	Called to clear all device input that has been buffered.

Support?		Yes

- DirectIO

Syntax 		LONG DirectIO (LONG Command, LONG* pData, BSTR* pString);

Remarks Call to communicate directly with the Service Object.

Support? 	No

Description	In the current, it implemented incompletely. We will improve it in the next release.

- ReleaseDevice 		Added in Release 1.5

Syntax 		LONG ReleaseDevice ();

Remarks 	Call this method to release exclusive access to the device.

Release 1.0 – 1.4

In releases prior to 1.5, this method is named Release.

Support?		Yes

- Close

Syntax 		LONG Close ();

Remarks 	Called to release the device and its resources.

Support?		Yes

- ResetStatistics  Added in Release 1.8

Syntax 		LONG ResetStatistics(BSTR m_StatisticsBuffer);

Remarks 	Called to Resets the defined resettable statistics in a device to zero.

Support?		No

- retrieveStatistics Added in Release 1.8

Syntax 		LONG RetrieveStatistics(BSTR* m_pStatisticsBuffer);

Remarks 	Called to Retrieves the requested statistics from a device.

Support?		No

- UpdateStatistics Added in Release 1.8

Syntax 		LONG UpdateStatistics(BSTR m_StatisticsBuffer);

Remarks 	Called to Updates the defined resettable statistics in a device.

Support?		No

- CompareFirmwareVersion

Syntax 	LONG CompareFirmwareVersion(BSTR m_FirmwareFileName, long* m_pResult);

Remarks 	Called to compare the firmware version with current firmware version of the device

Support?		No

- UpdateFirmware

Syntax 		LONG UpdateFirmware(BSTR m_FirmwareFileName);

Remarks 	Called to update current firmware.

Support?		No

- ClearInputProperties

Syntax 		void ClearInputProperties();

Remarks 	Sets all data properties that were populated as a result of firing a DataEvent or

ErrorEvent back to their default values.

Support?		Yes

- WriteTracks

Syntax 		long WriteTracks(LPCTSTR data, long timeout)

Remarks 	Sets all data properties that were populated as a result of firing a DataEvent or

ErrorEvent back to their default values.

Support?		NO

- AuthenticateDevice

Syntax 		long AuthenticateDevice (LPCTSTR response)

Remarks 	To authenticate a device, the application first calls the retrieveDeviceAuthenticationData method to retrieve a challenge token from the device. The application then typically passes this token to another entity that has special knowledge of a shared secret and is able to create a proper response token. This response token is then passed as the response parameter to this method and the service uses it to validate the authentication request. If this method succeeds, the device enters the authenticated state and the service sets the DeviceAuthenticated property to true.

For SecureMOIR:

The response need be 16 bytes in length. And it should be transmitted as a Hex string. Example, 0xAB 0x00 0x09 is converted to "AB0009".

Support ?	Yes.

- DeauthenticateDevice

Syntax 		long DeauthenticateDevice (LPCTSTR response)

Remarks 	This method is used to deauthenticate a device that is currently in the authenticated state (DeviceAuthenticated = true). The token is typically generated by passing the challenge retrieved from the retrieveDeviceAuthenticationData method to an entity that has special knowledge of a shared secret. If this method succeeds the service sets DeviceAuthenticated to false and enqueues a StatusUpdateEvent with status value set to MSR_SUE_DEVICE_DEAUTHENTICATED.

For SecureMOIR:

The response need be 16 bytes (when Encryption Algorithm is 3DES) or 8 bytes (when Encryption Algorithm is AES) in length. And it should be transmitted as a Hex string. Example, 0xAB 0x00 0x09 is converted to "AB0009".

Support ?	Yes

- RetrieveCardProperty

Syntax 		long RetrieveCardProperty (BSTR Name, BSTR *Value)

Remarks 	Retrieves the value of specific parsed properties from the last card swiped.

Support?		Yes

- RetrieveDeviceAuthenticationData

Syntax 		long RetrieveDeviceAuthenticationData (LPCTSTR challenge)

Remarks 	Applications call this method to retrieve a challenge token that will subsequently be used to generate response tokens that will be passed to the authenticateDevice and deauthenticateDevice methods. The challenge token is typically sent to another entity that has special knowledge of a shared secret that is required to generate the proper response token(s).

For SecureMOIR:

The got challenge is always 26 bytes in length. And it will be transmitted as a Hex string. Example, 0xAB 0x00 0x09 is converted to "AB0009".

Support?	    Yes

- UpdateKey

Syntax 		long UpdateKey (BSTR Key, BSTR KeyName)

Remarks 	Provides a new encryption key to the device. It is used only for those encryption algorithms in which new key values are sent to the terminal as a field in standard messages from the host.

For SecureMOIR:

KeyName can be set any value. The Key need be 16 bytes in length. And it should be transmitted as a Hex string. Example, 0xAB 0x00 0x09 is converted to "AB0009".

Support?		Yes.

## Events

These events are fired by the Service Object when it is necessary. The following functions are, in fact, the event-handlers that can be added into the applications. Then the applications can receive these events and do some processing accordingly. Please see UPOS Spec if the detailed information is wanted.

- DataEvent

Syntax 		void DataEvent (LONG Status);

The Status parameter contains the input status. Its value is Control-dependent,

and may describe the type or qualities of the input.

Remarks 	Fired to present input data from the device to the application.

Description 	a DataEvent can be received when a magnetic card is swiped if the three conditions are all met:

- DeviceEnabled = TRUE

- FreezeEvents = FALSE

- DataEventEnabled = TRUE.

The track data can be obtained , and the parsed data can also be obtained if ParseDecodeData is TRUE.

Support?		Yes

- DirectIO Event

Syntax 		void DirectIOEvent (LONG EventNumber, LONG* pData, BSTR* pString);

Parameter Description

EventNumber 	Event number. Specific values are assigned by the

Service Object.

pData 		Pointer to additional numeric data. Specific values vary

by EventNumber and the Service Object.

pString 		Pointer to additional string data. Specific values vary by

EventNumber and the Service Object.

Remarks 	Fired by a Service Object to communicate directly with the application.

Support?	 	No

Description	The event DirectIOEvent is used for some special communication between one SO and an application. In the current, it is implemented incompletely.

- Error Event

Syntax 		void ErrorEvent (LONG ResultCode, LONG ResultCodeExtended,

LONG ErrorLocus, LONG* pErrorResponse);

Parameter Description

ResultCode 		Result code causing the error event. See ResultCode

for values.

ResultCodeExtended 	Extended result code causing the error event. See

ResultCodeExtended for values.

ErrorLocus			Location of the error. See values below.

PErrorResponse		Pointer to the error event response. See values below.

when ErrorReportingType property is MSR_ERT_TRACK, and ErrorCode is E_EXTENDED, then ErrorCodeExtended contains Track-level status, broken down as follows:

Byte3	Byte2	Byte1	Byte0

Track 4 	Track 3 	Track 2 	Track 1

Remarks Fired when an error is detected and the Control’s State transitions into the error state.

NOTICE:  The error type is only one E_FAILURE (Other or general error) while any error is raised from reading card of SecureMOIR device, because the SecureMOIR hardware cannot distinguish the wrong type.

Support?		Yes

- StatusUpdate Event

Syntax 		void StatusUpdateEvent (LONG Status);

The Status parameter is for device class-specific data, describing the type of status change.

Remarks 	Fired when a Control needs to alert the application of a device status change.

Note	The SecureMOIR hardware cannot support the notification of power status change.

Support?	 	Yes

Description	It is not implemented by the SO for the power status cannot be inquired from the SecureMOIR.

# Programming Example

Three programming simple examples are described in this section including VC++6.0, VB6.0, and VS2005/2008/2010 C#, including the basic operation and event handle. In general, there are 2 steps: 1. Insert the OPOS Control Object (CO) into the project, 2. Add the event handle.

## Visual C++ 6.0 programming example

Windows XP Pro, Visual C++ 6.0, OPOS CO 1.13.  SO 1.13.201

- Install the OPOS driver d. And make sure the OPOS demo work.

- Create a “Dialog Based” MFC application by “MFC Application Wizard” with support “ActiveX Controls” in Visutal C++ 6.0.

- Select menu “Project/Add To Project/Components and Controls”, and select the folder “Registered ActiveX Controls”, then choose “OPOS MSR Control 1.13.001”, and insert this ActiveX control into project. Now there is an icon added in the “Controls” bar in the IDE.

- Add OPOS MSR CO to the dialog.

- Add DataEvent and ErrorEvent handle

void CMfc_diagDlg::OnDataEventMsr1(long Status)

- Add the variable by MFC Class Wizard in the tab “Member Variables”

- Add initialization code

void CMfc_diagDlg::OnButton1()

{

if (m_msr.Open("IDTECH_SMOIR_RS232")  == 0)

//0 is OPOS_SUCCESS

//" IDTECH_SMOIR_USBCDC" for USBCDC interface SecureMOIR device.

//" IDTECH_SMOIR_USBKB" for USBKB interface SecureMOIR device.

//" IDTECH_SMOIR_USBHID" for USBHID interface SecureMOIR device.

{

m_msr.ClaimDevice(100);

m_msr.SetDeviceEnabled(TRUE);

m_msr.SetDataEventEnabled(TRUE);

}

else {

// something wrong ...

}

}

- Handle DataEvent

void CMfc_diagDlg::OnDataEventMsr1(long Status)

{

MessageBox(m_msr.GetTrack1Data(), "Track 1 data");

m_msr.SetDataEventEnabled( TRUE); // prepare the next event.

}

- Running program. Click the “button1” to initialize the reader, and then swipe a card, it shows a message box to the track 1 data.

## Visual Basic 6.0 programming example

Windows XP Pro, Visual Basic 6.0, OPOS CO 1.13.  SO 1.13.201

1. Create a new “Standard EXE” project.

2. Insert the MSR ActiveX control from menu “Project/Components..”, and choose “OPOS MSR Control 1.13.001” in the tab “Controls”. Now there is an icon added in the control bar “General”.

3. Add this OPOS MSR control to “Form1” and double click this control to add “DataEvent” handle.

4. Initialization code:

Private Sub Form_Load()

OPOSMSR1.Open ("IDTECH_SMOIR_RS232")

//" IDTECH_SMOIR_USBCDC" for USBCDC interface SecureMOIR device.

//" IDTECH_SMOIR_USBKB" for USBKB interface SecureMOIR device.

//" IDTECH_SMOIR_USBHID" for USBHID interface SecureMOIR device.

OPOSMSR1.ClaimDevice (100)

OPOSMSR1.DeviceEnabled = True

OPOSMSR1.DataEventEnabled = True

End Sub

5. Event Handle

Private Sub OPOSMSR1_DataEvent(ByVal Status As Long)

MsgBox OPOSMSR1.Track1Data

OPOSMSR1.DataEventEnabled = True

End Sub

6. Running program, and swipe a card. It show track 1 data on a message box.

## Visual Studio 2005 C# programming example

Windows XP Pro, Visual Studio 2005 C#, OPOS CO 1.13.001 SO 1.13.201

1. Create a “Windows Application” Project.

2. Insert the “OPOS MSR Control 1.13.001” to the Toolbox: right click the tool bar “Toolbox” and select menu item “Choose item …”, and choose “OPOS MSR Control 1.13.001” in tab “COM Components”.

3. Add “OPOS MSR Control” to “Form1”, and double click it to add “DataEvent” handler code which is automotive generated by the wizard.

private void Form1_Load(object sender, EventArgs e)

{

if (axOPOSMSR1.Open("IDTECH_SMOIR_USBKB") == 0)

//0 is OPOS_SUCCESS

//" IDTECH_SMOIR_USBCDC" for USBCDC interface SecureMOIR device.

//" IDTECH_SMOIR_USBKB" for USBKB interface SecureMOIR device.

//" IDTECH_SMOIR_USBHID" for USBHID interface SecureMOIR device.

{

axOPOSMSR1.ClaimDevice(100);

axOPOSMSR1.DeviceEnabled = true;

axOPOSMSR1.DataEventEnabled = true;

}

}

private void axOPOSMSR1_DataEvent(object sender, AxOposMSR_1_13_Lib._IOPOSMSREvents_DataEventEvent e)

{

MessageBox.Show(axOPOSMSR1.Track1Data, "Track 1 data");

axOPOSMSR1.DataEventEnabled = true;

}

4. Running program, and swipe a card with some data in track 1.

# Result Code/Error Code List

const LONG OPOS_SUCCESS         =   0;

const LONG OPOS_E_CLOSED        = 101;

const LONG OPOS_E_CLAIMED       = 102;

const LONG OPOS_E_NOTCLAIMED    = 103;

const LONG OPOS_E_NOSERVICE     = 104;

const LONG OPOS_E_DISABLED      = 105;

const LONG OPOS_E_ILLEGAL       = 106;

const LONG OPOS_E_NOHARDWARE    = 107;

const LONG OPOS_E_OFFLINE       = 108;

const LONG OPOS_E_NOEXIST       = 109;

const LONG OPOS_E_EXISTS        = 110;

const LONG OPOS_E_FAILURE       = 111;

const LONG OPOS_E_TIMEOUT       = 112;

const LONG OPOS_E_BUSY          = 113;

const LONG OPOS_E_EXTENDED      = 114;