USER MANUAL

Spectrum Air

Outdoor Dual Headed

Magnetic-Only Insert Reader

TTL Interface

80116504-001-A

05-09-2013

Agency Approved

Specifications for subpart B of part 15 of FCC rule for a Class A computing device.

Limited Warranty

ID TECH warrants to the original purchaser for a period of 12 months from the date of invoice that this product is in good working order and free from defects in material and workmanship under normal use and service. ID TECH’s obligation under this warranty is limited to, at its option, replacing, repairing, or giving credit for any product which has, within the warranty period, been returned to the factory of origin, transportation charges and insurance prepaid, and which is, after examination, disclosed to ID TECH’s satisfaction to be thus defective. The expense of removal and reinstallation of any item or items of equipment is not included in this warranty. No person, firm, or corporation is authorized to assume for ID TECH any other liabilities in connection with the sales of any product. In no event shall ID TECH be liable for any special, incidental or consequential damages to Purchaser or any third party caused by any defective item of equipment, whether that defect is warranted against or not. Purchaser’s sole and exclusive remedy for defective equipment, which does not conform to the requirements of sales, is to have such equipment replaced or repaired by ID TECH. For limited warranty service during the warranty period, please contact ID TECH to obtain a Return Material Authorization (RMA) number & instructions for returning the product.

THIS WARRANTY IS IN LIEU OF ALL OTHER WARRANTIES OF MERCHANTABILITY OR FITNESS FOR PARTICULAR PURPOSE. THERE ARE NO OTHER WARRANTIES OR GUARANTEES, EXPRESS OR IMPLIED, OTHER THAN THOSE HEREIN STATED. THIS PRODUCT IS SOLD AS IS. IN NO EVENT SHALL ID TECH BE LIABLE FOR CLAIMS BASED UPON BREACH OF EXPRESS OR IMPLIED WARRANTY OF NEGLIGENCE OF ANY OTHER DAMAGES WHETHER DIRECT, IMMEDIATE, FORESEEABLE, CONSEQUENTIAL OR SPECIAL OR FOR ANY EXPENSE INCURRED BY REASON OF THE USE OR MISUSE, SALE OR FABRICATIONS OF PRODUCTS WHICH DO NOT CONFORM TO THE TERMS AND CONDITIONS OF THE CONTRACT.

©2012-2013 International Technologies & Systems Corporation. The information contained herein is provided to the user as a convenience. While every effort has been made to ensure accuracy, ID TECH is not responsible for damages that might occur because of errors or omissions, including any loss of profit or other commercial damage. The specifications described herein were current at the time of publication, but are subject to change at any time without prior notice.

ID TECH and Value through Innovation are registered trademarks of International Technologies & Systems Corporation.

Revision History

| Revision | Date | Description of Changes | By |
| --- | --- | --- | --- |
| A | 05/09/2013 | Initial Release | C.H. |

Table of Contents

1	INTRODUCTION	4

2	FEATURES	5

3	ABBREVIATIONS	6

4	RELATED DOCUMENTS	7

5	SPECIFICATION	8

6	CONNECTOR PINOUT	9

APPENDIX A	Envelope Drawing	11

APPENDIX B	Mounting Instruction	12

# INTRODUCTION

The Spectrum Air outdoor insert reader is designed for installations that might be subjected to harsh environments such as fuel pumps and outdoor kiosks. This insert reader meets IP 65 rating with dual head configurations supporting ISO and AAMVA encoded cards. A card is read by inserting it into and/or removing it out of the card slot.

# FEATURES

- Dual Head Magnetic only insert reader

- Interface: TTL

- IP 65 rating

- Reads up to 3 tracks of card data

- Sealed bezel and chassis – meaning that unit can allow water ingress but not allow water to seep into the host unit

- Ideal for gas pumps and outdoor kiosk applications

- Card seated switch

- 1 year Warranty

- Gas pump mounting – compatible with UIC/Panasonic mounting

- Mounting: Compatible with Panasonic ZU-1870MA8T2

# ABBREVIATIONS

AAMVA	American Association of Motor Vehicle Administration

ABA	American Banking Association

ASIC	Application Specific Integrated Circuit

BPI	Bits per Inch

CADL	California Drivers License Format (obsolete)

CE	European Safety and Emission approval authority

DC	Direct Current

ESD	Electro-Static Discharge

FCC	Federal Communications Commission

GND	Signal Ground

IPS	Inches per Second

ISO	International Organization for Standardization

mA	Milliamperes

msec	Milliseconds

MSR	Magnetic Stripe Reader

mV	Millivolts

POH	Powered On Hours

P/N	Part Number

RoHS	Restriction of Hazardous Substances

T1, T2, T3	Track 1 data, Track 2 data, Track 3 data

UV	Ultra Violet – spectrum of light rays

# RELATED DOCUMENTS

ISO 7810	Identification Cards - Physical Characteristics (1995)

ISO 7811	Identification Cards -Recording Technique (1995)

AAMVA	Best Practices Guidelines for the Use of Magnetic Stripes

ISO 4909	Magnetic stripe content for track 3

ISO 7812	Identification Cards – Identification for issuers Part 1 & 2

ISO 7813	Identification Cards – Financial Transaction Cards

# SPECIFICATION

Physical dimensions		: 120mm x 92mm x 48mm (LxWxH  with bezel)

Environments

Operating Temperature	: -20 °C to 70 °C (-4 °F to 158 °F)

Storage Temperature		: -40 °C to 70 °C (-40 °F to 158 °F)

Operating humidity		: 10% to 90% (no condensation allowed)

Storage humidity		: 10% to 90% (no condensation allowed)

Magnetic Reading

Reading direction		: Insertion / Withdrawal

Life of magnetic heads	: 1,000,000 operations minimum

Media Thickness		: 0.76mm (tolerance +- 0.08mm)

Swipe Speed			: 3 to 60 ips

ESD				: +- 8kV air discharge, contact +-4kV

Agency Approval		: FCC Class A, CE, RoHS

Power:

Input Voltage  (Vin)          :    DC +4.5V~ +5.5V

Maximum Input                 :    DC +6V

Power Consumption          :   < 20mA @ Vin = +5V

Interfaces, signals and main components:

Support interface               :   TTL

Signals                               :   TTL

# CONNECTOR PINOUT

2-Track Reader

| Wire Connection | Connector (3-641216-7 TE/AMP ) |
| --- | --- |
| Connector Pin No. | Signal | Description |  |
| 1 | Vin | Power Input: 5V |  |
| 2 | DA1 | Track1 Data: TTL Signal |  |
| 3 | CK1 | Track1 Clock: TTL Signal |  |
| 4 | DA2 | Track2 Data: TTL Signal |  |
| 5 | CK2 | Track2 Clock: TTL Signal |  |
| 6 | CLD | Card Load Detect: TTL Signal |  |
| 7 | GND | Power Ground |  |

3-Track Reader

For 3-track reader, use a connector that is different from the above. The pinout is as below:

| Wire Connection |
| --- |
| Connector Pin No. | Signal | Description |
| 1 | Vin | Power Input: 5V |
| 2 | DA1 | Track1 Data: TTL Signal |
| 3 | CK1 | Track1 Clock: TTL Signal |
| 4 | DA2 | Track2 Data: TTL Signal |
| 5 | CK2 | Track2 Clock: TTL Signal |
| 6 | CLD | Card Load Detect: TTL Signal |
| 7 | GND | Power Ground |
| 8 | CK3 | Reserved/Track3 Clock: TTL Signal |
| 9 | DA3 | Reserved/Track3 Data: TTL Signal |

Connector (3-641216-9  TE/AMP)

# APPENDIX A	Envelope Drawing

unit: mm, general tolerance: ±0.2mm

# APPENDIX B	Mounting Instruction