This device complies with Part 15 of the FCC Rules:

- This device may not cause harmful interference, and

- This device must accept any interference received, including interference that may cause undesired operation of the device.

Cautions and Warnings

|  | Caution: Danger of Explosion if battery is incorrectly charged. Use only standard USB 5V power source. Device contains a lithium battery. Approved temperature range for storage: -20℃ to +60℃. Disposal: Contact your local recycling center. |
| --- | --- |
|  | Warning: Avoid close proximity to radio transmitters, which may reduce the capabilities of the reader. |

UniPay 1.5 Quick Start

IDMR-AB83133/ IDMR-AB83133S

80131509-001

ID TECH

10721 Walker Street

Cypress, CA 90630

(714) 761-6368

www.idtechproducts.com

This device complies with Part 15 of the FCC Rules:

- This device may not cause harmful interference, and

- This device must accept any interference received, including interference that may cause undesired operation of the device.

Cautions and Warnings

|  | Caution: Danger of Explosion if battery is incorrectly charged. Use only standard USB 5V power source. Device contains a lithium battery. Approved temperature range for storage: -20℃ to +60℃. Disposal: Contact your local recycling center. |
| --- | --- |
|  | Warning: Avoid close proximity to radio transmitters, which may reduce the capabilities of the reader. |

UniPay 1.5 Quick Start

IDMR-AB83133/ IDMR-AB83133S

80131509-001

ID TECH

10721 Walker Street

Cypress, CA 90630

(714) 761-6368

www.idtechproducts.com

UniPay 1.5 is a mobile device for reading magnetic-stripe cards and EMV ("chip") cards.  In each shipment, you will receive a reader with a stability clip attached.  The stability clip can be removed by sliding it horizontally away from the audio jack.  To use the device, connect the UniPay 1.5 to the mobile device through the audio jack, or through a micro-USB cable (not included).  For optimal performance, set the headphone volume to its maximum.  The mobile device must have appropriate software installed in order to work with the UniPay 1.5.  Contact your UniPay 1.5 provider for applicable payment application(s).

Please note: This unit is delivered in a partially charged state. You should fully charge it before using it for the first time. Allow 2.5 hours for the initial charge.

To charge the unit: Use a USB to micro-USB cable (not included) to charge the unit. Note: The charging port is located on the side or bottom of the unit.  If you have the version with the bottom communication/charging port, the stability clip needs to be removed before charging.

 When the LED begins to flash green and amber, the unit is in a “low battery state” state and needs to be charged. LED status while charging:

Solid Amber: Battery is charging

Solid Green: Battery is Full (remove from charging)

LED status during transactions:

EMV transaction: flashes amber during transaction,

flashes green for 2 seconds when finished

Magnetic Stripe: solid green for successful swipe, solid red for unsuccessful swipe

FCC Regulatory Compliance

Notices: Class B Equipment

This equipment has been tested and found to comply with the limits for a Class B digital device pursuant to Part 15 of the FCC Rules. These limits are designed to provide reasonable protection against harmful interference in a residential installation. This equipment generates, uses, and can radiate radio frequency energy and, if not installed and used in accordance with the instructions, may cause harmful interference to radio communications. However, there is no guarantee that interference will not occur in a particular installation. This device complies with part 15 of the FCC rules. Operation is subject to two conditions: (1) This device may not cause harmful interference, and (2) this device must accept any interference received, including interference that may cause undesired operation.

If this equipment does cause harmful interference to radio or television reception, which can be determined by turning the equipment off and on, the user is encouraged to try to correct the interference by one or more of the following measures:

- Reorient or relocate the receiving antenna.

- Increase the separation between the equipment and the receiver.

- Connect the equipment into an outlet on a circuit different from that to which the receiver is connected.

- Consult the dealer or an experienced radio/TV technician for help.

Changes or modifications to the UniPay 1.5 not expressly approved by ID TECH could void the user's authority to operate the UniPay 1.5.

UniPay 1.5 is a mobile device for reading magnetic-stripe cards and EMV ("chip") cards.  In each shipment, you will receive a reader with a stability clip attached.  The stability clip can be removed by sliding it horizontally away from the audio jack.  To use the device, connect the UniPay 1.5 to the mobile device through the audio jack, or through a micro-USB cable (not included).  For optimal performance, set the headphone volume to its maximum.  The mobile device must have appropriate software installed in order to work with the UniPay 1.5.  Contact your UniPay 1.5 provider for applicable payment application(s).

Please note: This unit is delivered in a partially charged state. You should fully charge it before using it for the first time. Allow 2.5 hours for the initial charge.

To charge the unit: Use a USB to micro-USB cable (not included) to charge the unit. Note: The charging port is located on the side or bottom of the unit.  If you have the version with the bottom communication/charging port, the stability clip needs to be removed before charging.

 When the LED begins to flash green and amber, the unit is in a “low battery state” state and needs to be charged. LED status while charging:

Solid Amber: Battery is charging

Solid Green: Battery is Full (remove from charging)

LED status during transactions:

EMV transaction: flashes amber during transaction, flashes green for 2 seconds when finished

Magnetic Stripe: solid green for successful swipe, solid red for unsuccessful swipe

FCC Regulatory Compliance

Notices: Class B Equipment

This equipment has been tested and found to comply with the limits for a Class B digital device pursuant to Part 15 of the FCC Rules. These limits are designed to provide reasonable protection against harmful interference in a residential installation. This equipment generates, uses, and can radiate radio frequency energy and, if not installed and used in accordance with the instructions, may cause harmful interference to radio communications. However, there is no guarantee that interference will not occur in a particular installation. This device complies with part 15 of the FCC rules. Operation is subject to two conditions: (1) This device may not cause harmful interference, and (2) this device must accept any interference received, including interference that may cause undesired operation.

If this equipment does cause harmful interference to radio or television reception, which can be determined by turning the equipment off and on, the user is encouraged to try to correct the interference by one or more of the following measures:

- Reorient or relocate the receiving antenna.

- Increase the separation between the equipment and the receiver.

- Connect the equipment into an outlet on a circuit different from that to which the receiver is connected.

- Consult the dealer or an experienced radio/TV technician for help.

Changes or modifications to the UniPay 1.5 not expressly approved by ID TECH could void the user's authority to operate the UniPay 1.5.