ID TECH MSR OPOS 2.71

User’s Manual

Revised 11/5/2008

ID Technologies, Inc.

10721 Walker Street, Cypress CA 90630	Voice: (714) 761-6368 Fax: (714) 761-8880

Content

Revision History	2

ID TECH  SOFTWARE  COPYRIGHT  NOTICE	3

Description:	5

Important Note:	5

Target Device:	5

Platform:	5

Methods, Properties and Events Of MSR	5

Programming Example	5

Visual C++ 6.0 programming example.	6

Visual Basic 6.0 programming example.	8

Visual Studio 2005 C#  programming example	10

Result Code/Error Code List	10

Properties of MSR:	10

Methods of MSR:	16

Events of MSR:	19

# Revision History

| Revision Date | Description |
| --- | --- |
| 6/15/2005 | First draft release for internal review |
| 11/11/2005 | Modify for OPOS 2.00.000 |
| 12/14/2005 | V2.2, add version compatibility to firmware v1.30, v1.66, v1.69 |
| 1/24/2006 | V2.31 support USB HID KB connector |
| 2/21/2006 | V2.42 add supporting USB HID connector |
| 3/13/2006 | V2.43 add supporting USB RS232 connector |
| 5/19/2006 | Modify for v2.52 |
| 11/15/2006 | Update to 2.60 to support OPOS specification v1.10. |
| 10/18/2007 | Update to 2.70 |
| 6/26/08 | Add result code list, code exmaple of adding event. |
| 11/5/08 | Update to 2.71 |

# ID TECH  SOFTWARE  COPYRIGHT  NOTICE

Copyright 2005 International Technologies & Systems Corporation. All rights reserved. ID TECH is a registered trademark of International Technologies & Systems Corporation. Value through Innovation, MiniMag and EasyMag are trademarks of International Technologies & Systems Corporation.

ID TECH  SOFTWARE  LICENSE  AGREEMENT

ID TECH ("LICENSOR") IS WILLING TO LICENSE THIS SOFTWARE TO YOU ONLY IF YOU ACCEPT ALL OF THE TERMS IN THIS LICENSE AGREEMENT. PLEASE READ THE TERMS CAREFULLY BEFORE YOU AGREE BECAUSE YOU WILL BE BOUND BY THE TERMS OF THIS AGREEMENT. IF YOU DO NOT AGREE TO THESE TERMS, LICENSOR WILL NOT LICENSE THIS SOFTWARE TO YOU.

Ownership of the Software

1.  The Licensor software program ("Software") and any accompanying written materials are owned by Licensor [or its suppliers] and are protected by United States copyright laws, by laws of other nations, and by international treaties.

Grant Of License

2.  Licensor grants to you the right to use the Software in conjunction with an ID TECH product. You may load one copy into permanent memory of one computer and may use that copy only on that same computer.

Restrictions on Use and Transfer

3.  You may not copy the Software, except that (1) you may make one copy of the Software solely for backup or archival purposes, and (2) you may transfer the Software to a single hard disk provided you keep the original solely for backup or archival purposes. You may not copy the written materials.

4.  You may permanently transfer the Software and any accompanying written materials (including the most recent update and all prior versions) if you retain no copies and the transferee agrees to be bound by the terms of this Agreement. Such a transfer terminates your license. You may not rent or lease the Software or otherwise transfer or assign the right to use the Software, except as stated in this paragraph.

5.  You may not reverse engineer, decompile, or disassemble the Software.

Limited Warranty

6.  If used in conjunction with an ID TECH product, Licensor warrants that the Software will perform substantially in accordance with the accompanying written materials for a period of 90 days from the date of your receipt of the Software. Any implied warranties on the Software are limited to 90 days. Some states and territories do not allow limitations on duration of an implied warranty, so the above limitation may not apply to you.

7.  LICENSOR DISCLAIMS ALL OTHER WARRANTIES, EITHER EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO IMPLIED WARRANTIES OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE, AND NON-INFRINGEMENT, WITH RESPECT TO THE SOFTWARE AND ANY ACCOMPANYING WRITTEN MATERIALS. This limited warranty gives you specific legal rights. You may have others, which vary from state to state.

8.  LICENSOR'S ENTIRE LIABILITY AND YOUR EXCLUSIVE REMEDY SHALL BE REPLACEMENT OF THE SOFTWARE THAT DOES NOT MEET LICENSOR'S LIMITED WARRANTY. Any replacement Software will be warranted for the remainder of the original warranty period or 30 days, whichever is longer.

9.  This Limited Warranty is void if failure of the Software has resulted from modification, accident, abuse, or misapplication.

10.  IN NO EVENT WILL LICENSOR BE LIABLE TO YOU FOR DAMAGES, INCLUDING ANY LOSS OF PROFITS, LOST SAVINGS, OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES ARISING OUT OF YOUR USE OR INABILITY TO USE THE SOFTWARE. Because some states do not allow the exclusion or limitation of liability for consequential or incidental damages, the above limitation may not apply to you.

11.  This Agreement is governed by the laws of the state of California.

12. If you have any questions concerning this Agreement or wish to contact Licensor for any reason, please write: ID TECH, 10721 Walker Street, Cypress, CA 90630 or call (714) 761-6368.

13.  U.S. Government Restricted Rights. The Software and documentation are provided with Restricted Rights. Use, duplication, or disclosure by the Government is subject to restrictions set forth in subparagraph (c)(1) of The Rights in Technical Data and Computer Software clause at DFARS 252.227-7013 or subparagraphs (c)(1)(ii) and (2) of Commercial Computer Software - Restricted Rights at 48 CFR 52.227-19, as applicable. Supplier is ID TECH, 10721 Walker Street, Cypress, CA 90630.

# Description:

The documentation describes the properties, methods, and events by our MiniMag II MSR OPOS component. The component includes two parts: a Control Object running on the upper level, which is an ActiveX control, and a Service Control running on the lower level, which is an OLE automation server. The properties, methods, and events are exposed by the Control Object. For example, when the Control Object is imported into your project as an ActiveX control, you will see all the properties, methods, and events.

# Important Note:

For PS/2 keyboard or USB HID Keyboard interfaces, the standard keyboard should not be pressed when swiping cards, otherwise the card data will be wrong , MSR OPOS Driver will display a warning dialog and the data will be discarded .

Target Device: 
1. MiniMag II PS/2 Key Board Interface

2. MiniMag II USB HID KB Interface

3. MiniMag II USB HID Interface

4. MiniMag II RS232/USBCDC interface

Platform:
Microsoft Windows XP, 2000, 98
Service Object and Control Object:
	Service Object Version: 1.10.000  Dll File Version: 2.70
	Control Object Version:1.10.000

Methods, Properties and Events Of MSR

This section describe methods, properties, and events.

Programming Example

3 programming simple examples is describled in this section including VC++6.0, VB6.0, and VS2005 C#, including the basic operation and event handle. In general, there are 2 steps: 1. insert the OPOS Control Object (CO) into the project, 2. add the event handle.

Visual C++ 6.0 programming example.

Windows XP Pro, Visual C++ 6.0, OPOS CO 1.9. ID TECH SO 1.9.52

- Install the OPOS driver downed from web site www.idtechproducts.com. And make sure the OPOS demo work.

- Create a “Dialog Based” MFC application by “MFC Application Wizard” with support “ActiveX Controls” in Visutal C++ 6.0.

- Select menu “Project/Add To Project/Components and Controls”, and select the folder “Registered ActiveX Controls”, then choose “OPOS MSR Control 1.9.00”, and insert this ActiveX control into project. Now there is an icon added in the “Controls” bar in the IDE.

- Add OPOS MSR CO to the dialog.

- Add DataEvent and ErrorEvent handle

void CMfc_diagDlg::OnDataEventMsr1(long Status)

- Add the variable by MFC Class Wizard in the tab “Member Variables”

- Add initialization code

void CMfc_diagDlg::OnButton1()

{

if (m_msr.Open("IDTECH_MMII_USBHID")  == 0 /*OPOS_SUCCESS*/) {

m_msr.ClaimDevice(100);

m_msr.SetDeviceEnabled(TRUE);

m_msr.SetDataEventEnabled(TRUE);

}

else {

// something wrong ...

}

}

- Handle DataEvent

void CMfc_diagDlg::OnDataEventMsr1(long Status)

{

MessageBox(m_msr.GetTrack1Data(), "Track 1 data");

m_msr.SetDataEventEnabled( TRUE); // prepare the next event.

}

- running program. Click the “button1” to initialize the reader, and then swipe a card, it show a message box to the track 1 data.

Visual Basic 6.0 programming example.

Windows XP Pro, Visual Basic 6.0, OPOS CO 1.9. ID TECH SO 1.9.52

1. Create a new “Standard EXE” project.

2. Insert the MSR ActiveX control from menu “Project/Components..”, and choose “OPOS MSR Control 1.9.00” in the tab “Controls”. Now there is an icon added in the control bar “General”.

3. Add this OPOS MSR control to “Form1” and double click this control to add “DataEvent” handle.

4. Initialization code:

Private Sub Form_Load()

OPOSMSR1.Open ("IDTECH_MMII_USBHID")

OPOSMSR1.ClaimDevice (100)

OPOSMSR1.DeviceEnabled = True

OPOSMSR1.DataEventEnabled = True

End Sub

5. Event Handle

Private Sub OPOSMSR1_DataEvent(ByVal Status As Long)

MsgBox OPOSMSR1.Track1Data

OPOSMSR1.DataEventEnabled = True

End Sub

6. Running program, and swipe a card. It show track 1 data on a message box.

Visual Studio 2005 C#  programming example

Windows XP Pro, Visual Studio 2005 C#, OPOS CO 1.9. ID TECH SO 1.9.52

1. Create a “Windows Application” Project.

2. Insert the “OPOS MSR Control 1.9.00” to the Toolbox: right click the tool bar “Toolbox” and select menu item “Choose item …”, and choose “OPOS MSR Control 1.9.00” in tab “COM Components”.

3. Add “OPOS MSR Control” to “Form1”, and double click it to add “DataEvent” handler code which is automotive generated by the wizard.

private void Form1_Load(object sender, EventArgs e)

{

if (axOPOSMSR1.Open("IDTECH_MMII_USBHID") == 0 /* OPOS_SUCCESS */)

{

axOPOSMSR1.ClaimDevice(100);

axOPOSMSR1.DeviceEnabled = true;

axOPOSMSR1.DataEventEnabled = true;

}

}

private void axOPOSMSR1_DataEvent(object sender, AxOposMSR_1_9_Lib._IOPOSMSREvents_DataEventEvent e)

{

MessageBox.Show(axOPOSMSR1.Track1Data, "Track 1 data");

axOPOSMSR1.DataEventEnabled = true;

}

4. Running program, and swipe a card with some data in track 1.

Result Code/Error Code List

const LONG OPOS_SUCCESS         =   0;

const LONG OPOS_E_CLOSED        = 101;

const LONG OPOS_E_CLAIMED       = 102;

const LONG OPOS_E_NOTCLAIMED    = 103;

const LONG OPOS_E_NOSERVICE     = 104;

const LONG OPOS_E_DISABLED      = 105;

const LONG OPOS_E_ILLEGAL       = 106;

const LONG OPOS_E_NOHARDWARE    = 107;

const LONG OPOS_E_OFFLINE       = 108;

const LONG OPOS_E_NOEXIST       = 109;

const LONG OPOS_E_EXISTS        = 110;

const LONG OPOS_E_FAILURE       = 111;

const LONG OPOS_E_TIMEOUT       = 112;

const LONG OPOS_E_BUSY          = 113;

const LONG OPOS_E_EXTENDED      = 114;

Properties of MSR:

Please see UPOS Spec if the detailed information is wanted.

NOTE: 	CO --- Control Object

SO --- Service Object

AP or App --- the abbreviation of Application.

| Name | Type | Mutability | Use After | Description | Support? |
| --- | --- | --- | --- | --- | --- |
| DeviceControlDescription | String | read-only | -- | Identify the Control Object and the company that produced it | Yes |
| DeviceControlVersion | int32 | read-only | -- | hold the Control Object version number. | Yes |
| DeviceServiceDescription | String | read-only | open | identify the Service Object supporting the device and the company that produced it | Yes |
| DeviceServiceVersion | int32 | read-only | open | hold the Service Object version number. | Yes |
| PhysicalDeviceDescription | string | read-only | open | identify the device and any pertinent information about it. | Yes |
| PhysicalDeviceName | string | read-only | open | identify the device and any pertinent information about it. | Yes |

Property Group1---Description

Property Group2---Control

| Name | Type | Mutability | Use After | Description | Support? |
| --- | --- | --- | --- | --- | --- |
| Claimed | Boolean | read-only | open | MiniMag must be claimed for exclusive use before access its methods and properties, and before any events to be fired. It is initialized to FALSE by the Open method. It is set to TRUE after the method Claim is successfully called. | Yes |
| AutoDisable | Boolean | read-write | open | When TRUE, as soon as an event DataEvent is received, then DeviceEnabled is automatically to FALSE. It is initialized to FALSE by the Open method. | Yes |
| DeviceEnabled | Boolean | read-write | open& claim | When FALSE, MiniMag has been disabled and any subsequent input will be discarded (No DataEvent could be received even if the card is swiped). It is initialized to FALSE by the Open method. | Yes |
| FreezeEvents | boolean | read-write | open | When TRUE, events are not required to be delivered and will be held by SO until events are unfrozen. It is initialized to FALSE by the Open method. | Yes |
| DataEventEnabled | boolean | read-write | open | When TRUE, a DataEvent or ErrorEvent will be delivered immediately when had. (Of course , FreezeEvents=FALSE and DeviceEnabled=TRUE is a prerequisit). It is initialized to FALSE by the Open method. | Yes |
| CapPowerReporting | int32 | read-only | open | Identifies the reporting capabilities of the device about Power. It seems that MiniMag doesn’t support in the hardware. | No |
| PowerNotify | int32 | read-write | open | Contains the type power notification selection made by the Application. is initialized to OPOS_PN_DISABLED by the Open method. | No |
| PowerState | int32 | read-only | open | Contains the current power condition. It seems that MiniMag doesn’t support in the hardware. | No |
| State | int32 | Read-only | -- | Contains the current state of the Control. It can be set to one of the four values: Closed, Idle, Busy, or Error. | Yes |
| DataCount | int32 | Read-only | open | Holds the number of enqueued DataEvents remained in the queue. | Yes |
| CheckHealthText | string | read-only | open | Holds the results of the most recent call to the CheckHealth method. Before the first CheckHealth method call, its value is uninitialized. | Yes |

Property Group3---Track Control

| Name | Type | Mutability | Use After | Description | Support? |
| --- | --- | --- | --- | --- | --- |
| CapISO | boolean | read-only | open | If TRUE, MiniMag supports ISO cards. | Yes |
| CapJISOne | boolean | read-only | open | If TRUE, MiniMag supports JIS Type-I cards. JIS-I cards are a superset of ISO cards. Therefore, if CapJISOne is true, it is implied that CapISO is also TRUE. | Yes |
| CapJISTwo | boolean | read-only | open | If TRUE, MiniMag supports JIS type-II cards. | Yes |
| CapTransmitSentinels | boolean | read-only | open | If TRUE, MiniMag is able to transmit the start and end sentinels. e.g. start sentinel could be ‘%’ or ‘;’, and stop sentinel could be ‘?’. | Yes |
| DecodeData | boolean | read-write | open | If TRUE, each byte of track data properties is mapped from its original encoded bit sequence (as it exists on the magnetic card) to its corresponding decoded ASCII bit sequence. | Yes |
| ParseDecodeData | boolean | read-write | open | When TRUE, the decoded data contained within the Track1Data and Track2Data properties is further separated into fields for access via various other properties. If DecodeData=FALSE, ParseDecodeData must be false. | Yes |
| TransmitSentinels | boolean | read-write | open | If TRUE, the Track1Data, Track2Data, Track3Data, and Track4Data properties contain start and end sentinel values. Otherwise only the track data between these sentinels. | Yes |
| TracksToRead | int32 | read-write | open | Indicate which track data that the App wishes to get following a card sweep. | Yes |
| ErrorReportingType | int32 | Read-write | open | Holds the type of errors to report via ErrorEvents. This property has one of the following values: MSR_ERT_CARD or MSF_ERT_TRACK | Yes |

Property Group4---TrackData

| Name | Type | Mutability | Use After | Description | Support? |
| --- | --- | --- | --- | --- | --- |
| Track1Data | binary | read-only | open | Holds the track 1 data obtained from the most recently swept card. If DecodeData is true, then it has been decoded from the “raw” format. it may also be parsed into other properties when the ParseDecodeData property is set. | Yes |
| Track1DiscretionaryData | binary | read-only | open | Holds the track 1 discretionary data obtained from the most recently swept card. It may be NULL when: 1) The field was not included in the track data obtained, or, 2) The track data format was not supported, 3) ParseDecodeData is false. | Yes |
| Track2Data | binary | read-only | open | Holds the track 2 data obtained from the most recently swept card. If DecodeData is true, then it has been decoded from the “raw” format. it may also be parsed into other properties when the ParseDecodeData property is set. | Yes |
| Track2DiscretionaryData | binary | read-only | open | Holds the track 2 discretionary data obtained from the most recently swept card. It may be NULL when: 1) The field was not included in the track data obtained, or, 2) The track data format was not supported, 3) ParseDecodeData is false. | Yes |
| Track3Data: | binary | read-only | open | Holds the track 3 data obtained from the most recently swept card. | Yes |
| Track4Data | binary | read-only | open | Holds the track 4 data (JIS-II) obtained from the most recently swept card. | Yes |

Property Group5---ParsedData

| Name | Type | Mutability | Use After | Description | Support? |
| --- | --- | --- | --- | --- | --- |
| AccountNumber | string | read-only | Open | Holds the account number obtained from the most recently swept card. it is initialized to NULL if: 1) The field was not included in the track data obtained, or, 2) The track data format was not suported, or, 3) ParseDecodeData is false. | Yes |
| ExpirationData | string | read-only | Open | Holds the expiration date obtained from the most recently swept card. Others are same as AccountNumber. | Yes |
| FirstName | string | read-only | Open | Holds the first name obtained from the most recently swept card. Others are same as AccountNumber. | Yes |
| MiddleInitial | string | read-only | Open | Holds the middle initial obtained from the most recently swept card. Others are same as AccountNumber. | Yes |
| Surname | string | read-only | Open | Holds the surname obtained from the most recently swept card. Others are same as AccountNumber. | Yes |
| Title | string | read-only | Open | Holds the title obtained from the most recently swept card.. Others are same as AccountNumber. | Yes |
| Suffix | string | read-only | Open | Holds the suffix obtained from the most recently swept card.. Others are same as AccountNumber. | Yes |
| ServicCode | string | read-only | Open | Holds the service code obtained from the most recently swept card. Others are same as AccountNumber. | Yes |

Property Group6--- Statistic

| Name | Type | Mutability | Use After | Expected Result | Test Result |
| --- | --- | --- | --- | --- | --- |
| CapStatisticsReporting | boolean | read-write | Open | If true ,the SO can get device information to a XML statistics | No |
| CapUpdateStatistics | Bolean | read-write | Open | If true ,the SO can update the XML statistics | No |

Property Group7---Firmware

| Name | Type | Mutability | Use After | Expected Result | Test Result |
| --- | --- | --- | --- | --- | --- |
| CapCompareFirmwareVersion | boolean | read-write | Open | If true ,the SO can compare the Firmware version | No |
| CapUpdateFirmware | boolean | read-write | Open | If true ,the SO can update the firmware of the device | No |
| CapWritableTracks | Int32 | Read_only | Open | This capability indicates if the MSR device supports the writing of track data - and which tracks are supported. | NONE |
| EncodingMaxLength | Int32 | Read_only | Open | The maximum length of data that can be written by the MSR to the track(s) . | NO |
| TracksToWrite | Int32 | Read-Write | Open | Holds the MSR track(s) that will be written. | NO |

## Methods of MSR:

These function declarations may be different when the Control Object(OPOSMSR.OCX) is imported into your application project. Please see UPOS Spec if the detailed information is wanted.

1)Open

Syntax 		LONG Open (BSTR DeviceName);

Remarks 	Call to open a device for subsequent I/O.

Device Name:

PS2 Keyboard Interfae:	 "IDTECH_MMII_PS/2KB"

USB HID KB interface:  "IDTECH_MMII_USBKB" or "IDTechMiniMagII"

USB HID interface		 "IDTECH_MMII_USBHID"

RS232 interface		 "IDTECH_MMII_RS232"

USBCDC interface		 “IDTECH_MMII_USBCDC” or

“IDTECH_MMII_RS232

Support?		Yes

This method find more parameters in the Windows Register Tables on key or subkeys:

HKEY_LOCAL_MACHINE\Software\OLEforRetail\ServiceOPOS\MSR\xxxInfterface

RS232 interface and USBCDC interface:

Subkey: Connector

Key value name: CONNECTOR

Key value: "COM1/baud=9600/parity=N/data=8/stop=1"

COM1 specify the serial port name, if the device is plugged in the second port, it should modified as "COM2". The rest settings should be right defined according to the settings of the reader.

Key value Name: COM1, this name should be same the first filed of CONNECTOR key value. The field is separated by "/". So, if the reader is changed to other port, this key value is needed modified also.

USB HID interface:

Subkey: Connector:

Key value name: CONNECTOR

Key value: USBHID/0acd/0500

First field USBHID specify the type of the connector. 0acd is the USB device vendor  ID, 0500 is the reader product ID for USB HID connector device.

USB HID KB interface:

Subkey: Connector:

Key value name: CONNECTOR

Key value: USBHID/0acd/0520

First field USBHID specify the type of the connector. 0acd is the USB device vendor  ID, 0520 is the reader product ID.

PS2 keyboard interface:

Subkey: Connector:

Key value name: CONNECTOR

Key value: PS2

2)ClaimDevice 	Added in Release 1.5

Syntax 		LONG ClaimDevice (LONG Timeout);

Remarks 	Call this method to request exclusive access to the device. Many devices require

an application to claim them before they can be used.  Release 1.0 – 1.4 In releases prior to 1.5, this method is named Claim.

Support?		Yes

3)CheckHealth

Syntax 		LONG CheckHealth (LONG Level);

Remarks 	Called to test the state of a device.

Support? 	Yes

Description	When select CH_INTERNAL, SO will return the firmwareversion of the Msr device, if not it tells that there is something wrong with the device . CheckHealthText property will be  “Internal HCheck: Successful” ,if reading the firmware version is successful .

When select CH_EXTERNAL,SO will display a swiping card dialog ,it will display the “Real data ” of the card , include Start Sentinel and End Sentinel. CheckHealth Text property will show “External HCheck:: HCheck: Complete” , after close the dialog .

When select CH_INTERACTIVE , SO will display a dialog , which include firmware version and swiping card .CheckHealthText property will show “External HCheck:: HCheck: Complete” , after close the dialog .

4)ClearInput

Syntax 		LONG ClearInput ();

Remarks 	Called to clear all device input that has been buffered.

Support?		Yes

5)DirectIO

Syntax 		LONG DirectIO (LONG Command, LONG* pData, BSTR* pString);

Remarks Call to communicate directly with the Service Object.

Support? 	Yes

Description	In the current, it implemented incompletely. We will improve it in the next release.

6)ReleaseDevice 		Added in Release 1.5

Syntax 		LONG ReleaseDevice ();

Remarks 	Call this method to release exclusive access to the device.

Release 1.0 – 1.4

In releases prior to 1.5, this method is named Release.

Support?		Yes

7)Close

Syntax 		LONG Close ();

Remarks 	Called to release the device and its resources.

Support?		Yes

8) ResetStatistics  Added in Release 1.8

Syntax 		LONG ResetStatistics(BSTR m_StatisticsBuffer);

Remarks 	Called to Resets the defined resettable statistics in a device to zero.

Support?		No

9) retrieveStatistics Added in Release 1.8

Syntax 		LONG RetrieveStatistics(BSTR* m_pStatisticsBuffer);

Remarks 	Called to Retrieves the requested statistics from a device.

Support?		No

10) UpdateStatistics Added in Release 1.8

Syntax 		LONG UpdateStatistics(BSTR m_StatisticsBuffer);

Remarks 	Called to Updates the defined resettable statistics in a device.

Support?		No

11) CompareFirmwareVersion

Syntax 		LONG CompareFirmwareVersion(BSTR m_FirmwareFileName, long* m_pResult);

Remarks 	Called to compare the firmware version with current firmware version of the device

Support?		No

12) UpdateFirmware

Syntax 		LONG UpdateFirmware(BSTR m_FirmwareFileName);

Remarks 	Called to update current firmware.

Support?		No

13) ClearInputProperties

Syntax 		void ClearInputProperties();

Remarks 	Sets all data properties that were populated as a result of firing a DataEvent or

ErrorEvent back to their default values.

Support?		Yes

14) WriteTracks

Syntax 		long WriteTracks(LPCTSTR data, long timeout)

Remarks 	Sets all data properties that were populated as a result of firing a DataEvent or

ErrorEvent back to their default values.

Support?		NO

## Events of MSR:

These events are fired by the Service Object when it is necessary. The following functions are, in fact, the event-handlers that can be added into the applications. Then the applications can receive these events and do some processing accordingly. Please see UPOS Spec if the detailed information is wanted.

1)DataEvent

Syntax 		void DataEvent (LONG Status);

The Status parameter contains the input status. Its value is Control-dependent,

and may describe the type or qualities of the input.

Remarks 	Fired to present input data from the device to the application.

Description 	a DataEvent can be received when a magnetic card is swiped if the three conditions are all met:

- DeviceEnabled = TRUE

- FreezeEvents = FALSE

- DataEventEnabled = TRUE.

The track data can be obtained , and the parsed data can also be obtained if ParseDecodeData is TRUE.

Support?		Yes

2)DirectIO Event

Syntax 		void DirectIOEvent (LONG EventNumber, LONG* pData, BSTR* pString);

Parameter Description

EventNumber 	Event number. Specific values are assigned by the

Service Object.

pData 		Pointer to additional numeric data. Specific values vary

by EventNumber and the Service Object.

pString 		Pointer to additional string data. Specific values vary by

EventNumber and the Service Object.

Remarks 	Fired by a Service Object to communicate directly with the application.

Support?	 	No

Description	The event DirectIOEvent is used for some special communication between one SO and an application. In the current, it is implemented incompletely.

3)Error Event

Syntax 		void ErrorEvent (LONG ResultCode, LONG ResultCodeExtended,

LONG ErrorLocus, LONG* pErrorResponse);

Parameter Description

ResultCode 		Result code causing the error event. See ResultCode

for values.

ResultCodeExtended 	Extended result code causing the error event. See

ResultCodeExtended for values.

ErrorLocus			Location of the error. See values below.

PErrorResponse		Pointer to the error event response. See values below.

when ErrorReportingType property is MSR_ERT_TRACK, and ErrorCode is E_EXTENDED, then ErrorCodeExtended contains Track-level status, broken

down as follows:

Byte3	Byte2	Byte1	Byte0

Track 4 	Track 3 	Track 2 	Track 1

Remarks Fired when an error is detected and the Control’s State transitions into the error state.

Support?		Yes

4)StatusUpdate Event

Syntax 		void StatusUpdateEvent (LONG Status);

The Status parameter is for device class-specific data, describing the type of status change.

Remarks 	Fired when a Control needs to alert the application of a device status change.

Note	The MiniMag hardware cannot support the notification of power status change.

Support?	 	No

Description	It is not implemented by the SO for the power status cannot be inquired from the MiniMag.